## Slide 1: WNYRIC Standards Committee
Bonjour Best Practices

## Slide 2: Bonjour
Bonjour, also known as zero-configuration networking, enables automatic discovery of computers, devices, and services on IP networks. Bonjour uses industry standard IP protocols to allow devices to automatically discover each other without the need to enter IP addresses or configure DNS servers. Specifically, Bonjour enables automatic IP address assignment without a DHCP server, name to address translation without a DNS server, and service discovery without a directory server. Bonjour is an open protocol which Apple has submitted to the IETF as part of the ongoing standards-creation process.
  Bonjour lets you connect a printer to your network without the need to assign it a specific IP address or manually enter that address into each computer. With zero-configuration networking, nearby computers can discover its existence and automatically determine the printer’s IP address. And if that address is a dynamically assigned address that changes, they can automatically discover the new address in the future.

## Slide 3: Bonjour – mDNS Requests
In large network environments where there are many service requests from many users and applications, a flood of responses from multitudes of servicing devices will occur.
  “Server-free addressing, naming, and service discovery have the potential to create a significant amount of excess network traffic, but Bonjour takes a number of steps to reduce this traffic to a minimum. … Bonjour makes use of several mechanisms for reducing zero-configuration overhead, including caching, suppression of duplicate responses, exponential back-off, and service announcement”
Even with this suppression, there is still a need for network design considerations to further reduce this traffic, lest it overwhelm the existing infrastructure.
Notes: “Multicast applications such as Bonjour require special consideration when being deployed over a wireless network since a multicast in 802.11 is essentially sent out as a broadcast so all clients can hear it”

## Slide 4: Bonjour – mDNS Requests
In a modern well-designed wired network, there should be ample capacity to handle a large-scale Bonjour deployment
There are concerns with the way multicasts and broadcasts are handled on a wireless network.
  On a wireless network, every device will connect with a best bandwidth effort attachment, depending upon distance from the wireless access point (AP) and wireless frequency spectrum conditions such as interference. A device may quite possibly connect at the lowest allowed bandwidth setting of the overall wireless network.
The mDNS traffic will be generated at the rate of the lowest common bandwidth of connected devices.
Notes: When many devices are generating mDNS traffic, the wireless network performance will degrade and the network will become overwhelmed. “… the network is flooded with mDNS traffic that consumes valuable wireless airtime. Network administrators are faced with a difficult choice between propagating mDNS traffic across VLANs – and risking a significant reduction in wireless performance – or blocking mDNS traffic to prevent connectivity for Bonjour-capable devices and services. [emphasis added]”
Subsequently, the mDNS traffic will be generated at the rate of the lowest common bandwidth of connected devices. As the wireless network transmits the mDNS traffic, all devices are limited to the bandwidth speed of the slowest connection. When many devices are generating mDNS traffic, the wireless network performance will degrade and the network will become overwhelmed. “… the network is flooded with mDNS traffic that consumes valuable wireless airtime.
Network administrators are faced with a difficult choice between propagating mDNS traffic across VLANs – and risking a significant reduction in wireless performance – or blocking mDNS traffic to prevent connectivity for Bonjour-capable devices and services. [emphasis added]”

## Slide 5: Bonjour - Availability
Another issue for network administrators to resolve is what services are available to which users on different subnets and providing an understandable device name.
  This feature of the protocol creates a problem for a segmented network.
Therefore, without some form of intervention, users will not see services available on other subnets in a segmented network.

## Slide 6: Bonjour Gateways
A “Bonjour gateway” can be deployed on multiple subnets to listen to all the mDNS requests and responses.
  Bonjour services can be accessed even when the Bonjour device is connected via an Ethernet cable on a network. The VLAN of wired Bonjour devices must be trunked to the [wireless] controller so that their advertisements can be seen and sent out to wireless clients
In general, the Bonjour gateway will build a table of devices, services, and IP addresses of the subnets it is connected.

## Slide 7: Bonjour Gateways
Cisco’s Bonjour gateway, also known more formally as Cisco Service Discovery Gateway, has been introduced in version 7.4 of its wireless controller.
Aruba Networks has introduced its Bonjour gateway in 2012.
Aerohive Networks support a Bonjour gateway, but they also make a free version available to overlay other vendor networks.
  The free Bonjour Gateway supports propagating up to 500 Bonjour services.
Avaya is planning a Bonjour Gateway for Q1 2014
Notes: There are no VLAN limitations, however the 500 services limit includes VLANs re-advertisements. For example, if you have 50 services on VLAN 10 that need to be propagated to two other subnets corresponding to VLAN 20 and VLAN 30, then you’d already be consuming (50 x 3) = 150 services” (Aerohive FAQ, p. 4). In addition to the major vendors, there are a host of niche providers making Bonjour gateways for specific purposes, primarily for print services.

## Slide 8: Bonjour Options
Do nothing.
Disable/suppress multicast traffic on wireless access points (WAP) or network switch.
Put all mDNS enabled devices on a wired network (turn off wireless options, ensuring access via one and only one subnet).
Deploy a third party overlay Bonjour gateway to your existing network
Deploy a wireless controller and/or wired switch with an integrated Bonjour/mDNS gateway.
Notes: Do nothing.
  The network may not have critical mass for Bonjour to be an issue. Due to the "automagical" nature of Bonjour, users are just using the services available with no problems or concerns.
Disable/suppress multicast traffic on wireless access points (WAP) or network switch.
  Benefit: This will preserve wireless bandwidth capacity and integrity.
  Disadvantage: Will not be able to use new and emerging technologies.
Put all mDNS enabled devices on a wired network (turn off wireless options, ensuring access via one and only one subnet).
  Benefit: The wired Ethernet network has better capacity to handle the Bonjour traffic. This option will work well for Apple TV, Air Print, security cameras, and printers, all which have a wired Ethernet connector.
  Disadvantage: This will only work with devices on the same subnet, without implementing a Bonjour gateway. Wireless devices will not see wired devices unless a Bonjour gateway is installed.
Deploy a third party overlay Bonjour gateway to your existing network
  Benefit: This will allow mDNS to ‘work’ over a wired and wireless subnet. This option will overlay current network infrastructure.
  Benefit: Third party products, which are function specific, can provide solutions at a low cost.
  Disadvantage: Third party products lend itself to be implanted in a haphazard manner, due to a variety of low cost solutions and inadequate design. Furthermore, these products typically do not help with wireless congestion.
Deploy a wireless controller and/or wired switch with an integrated Bonjour/mDNS gateway.
  Benefit: This option has the ability to scale over many subnets. Some systems have the ability to suppress mDNS service responses without turning off multicast. Most systems will reduce wireless multicast traffic. Some systems have the ability to create specific access lists such as limiting resources to/from devices and locations, and/or integrate with a network authentication system.
  Disadvantage: The existing wired/wireless system may need upgrades or be replaced to support Bonjour/mDNS gateway functionality.
    Cisco requires version 7.4.
    Aruba requires version 6.1.5
    Supported by current cloud controllers of Meraki and Aerohive.

## Slide 9: Bonjour Best Practices
Embrace the technology.
  mDNS and Bonjour are not going away.
Create Bonjour access policies.
  Understand the devices and the services that can be provided and utilized such as printers, Apple TVs, servers and iTunes.
Periodically inventory Bonjour use on the network.
  Use available Bonjour browsers or implemented Bonjour gateways to see what is on the network.
Have a device naming structure that is clear and consistent for the organization and for users.
  Use unique and contextual names such as Apple TV Room 123.
Notes: Embrace the technology. mDNS and Bonjour are not going away. Furthermore, mDNS works well in an IPv6 environment (the next evolution of IP networking). Even if IPv6 isn’t actively deployed in the network, it is being used. The same self assigned IP addressing techniques work for IPv6 and is running on the network with newer devices.
Create Bonjour access policies. Understand the devices and the services that can be provided and utilized such as printers, Apple TVs, servers and iTunes. Plan for the context of services the users should be able to see and where to use them. “Limit Bonjour traffic by ownership and location to ensure a better user experience. Campus networks can have hundreds, if not thousands of Bonjour-capable devices. It is likely that not all these devices are for every individual” (Aruba, p. 3).
Periodically inventory Bonjour use on the network. Use available Bonjour browsers or implemented Bonjour gateways to see what is on the network. Know what services are intended and be aware of ones that just show up.
Have a device naming structure that is clear and consistent for the organization and for users. For example Apple TV-1 and Apple TV-2 do not have much context if 50 are deployed throughout the campus. Instead, use unique and contextual names such as Apple TV Room 123.

## Slide 10: Bonjour Best Practices
Evolve the network design to incorporate Bonjour according to the access policies.
  Understand the wireless network coverage areas and its limitations.
Implement a network solution that fits the need of Bonjour users.
  New infrastructure or overlay prior to critical failure.
Segment the network appropriately.
  Smaller network segments will naturally reduce the amount of Bonjour traffic on the subnet.
Tune the wireless network for optimal performance.
  Tuning may include deploying more access points and/or relocating them, to avoid devices connecting at low data rates.
Notes: Evolve the network design to incorporate Bonjour according to the access policies. Understand the wireless network coverage areas and its limitations. Take care to allow guest and/or presenters access to highly visible areas such as lecture halls and auditoriums, where screen broadcasting is likely to require an Apple TV.
Implement a network solution that fits the need of Bonjour users. Whether it is new infrastructure or deploying an overlay system till such time the existing network can be upgraded, something should be done before critical failure force network changes.
There are some specific network design parameters to ensure success with enabling mDNS/Bonjour.
Segment the network appropriately. Smaller network segments will naturally reduce the amount of Bonjour traffic on the subnet. “If you want to control mDNS/Bonjour, the key is to limit the size of the local segment [emphasis added]” (Cisco 7.4, p. 4).
Tune the wireless network for optimal performance. Tuning may include deploying more access points and/or relocating them, to avoid devices connecting at low data rates. “Multicast applications such as Bonjour require special consideration when being deployed over a wireless network since a multicast in 802.11 is essentially sent out as a broadcast so all clients can hear it. … In order to optimize the delivery of these frames, it is important to tune the 802.11 data rates within the controller to allow multicast to be delivered at the highest rate that the coverage model of the network can support” (Cisco ID: 113443, p.3).

## Slide 11: Bonjour Best Practices
Put Bonjour devices on a wired network.
  mDNS traffic can be reduced by segregating these devices onto a different network segment from the wireless.
Deploy a Bonjour gateway.
  Trunk all VLANs to devices that can report mDNS requests and responses to the gateway.
Suppress mDNS responders through the wireless network.
  Limit Bonjour traffic over the wireless LAN (WLAN) to prevent performance issues.
Determine if Wide Area Bonjour is appropriate for the network.
Track the amount of IP addresses being taken up by mobile devices.
Notes: Put Bonjour devices on a wired network. Most devices such as iPads will not go on a wired network, as they are wireless access only. But printers and security cameras have wired network connectors built in. mDNS traffic can be reduced by segregating these devices onto a different network segment from the wireless devices. Of course, this model requires deployment of a Bonjour gateway.
Deploy a Bonjour gateway. Trunk all VLANs to devices that can report mDNS requests and responses to the gateway. By doing this, all services can be discovered, advertised, and controlled as needed.
Suppress mDNS responders through the wireless network. Create access control lists to announce only services that should be advertised. “Limit Bonjour traffic over the wireless LAN (WLAN) to prevent performance issues. Multicast traffic by default goes out on all Wi-Fi access points (APs) and often at the lowest rates, taking up valuable airtime. [Emphasis added]” (Aruba, p. 3).
Determine if Wide Area Bonjour is appropriate for the network. “Starting in Mac OS X v10.4 Tiger and Bonjour for Windows, a network administrator can set up a Bonjour name server to enable wide-area capable devices and applications to discover services anywhere in the world. … You can also use Linux, Solaris, or any other Unix-style operating system that can run the BIND name server. ... Wide-Area Bonjour uses DNS Service Discovery [DNS-SD] along with DNS Update [RFC 2136] and TSIG security [RFC 2845]. Mac OS X Tiger (and most Linux distributions) include the standard BIND DNS Server (named), which supports DNS Update” (dns-sd.org, Server Setup).
Track the amount of IP addresses being taken up by mobile devices. This is not limited to Bonjour capable devices but any smart device that enters your building. Even if they are not actively being used, the presence of a mobile device may cause an IP address assigned to it. This could cause a shortage of available addresses for desired use.

## Slide 12: Bonjour Summary
Bonjour Paper – Mat Dzuiba 06/2013
Additional whitepapers from Cisco, Aruba, Aerohive for research
Questions?